EMERGENCY SOLUTIONS GRANT PROGRAM

LEAD-BASED PAINT REQUIREMENTS FOR SHELTERS

| TYPE OF PROJECT | CONSTRUCTION PERIOD | REQUIREMENTS |
| --- | --- | --- |
| Rehabilitation of property receiving less than $5,000 assistance per unit | Pre-1978 | Provision of pamphlet Conduct paint testing of surfaces to be disturbed Implement safe work practices during rehab Clearance examination of work site Notice to Occupants of finished testing |
| Rehabilitation on property receiving more than $5,000 and up to $25,000 per unit | Pre-1978 | Provision of pamphlet Conduct paint testing of surfaces to be disturbed Risk Assessment Interim controls Notice to Occupants |
| Rehabilitation on property receiving more than $25,000 per unit | Pre-1978 | Provision of pamphlet Conduct paint testing of surfaces to be disturbed Risk assessment Abatement of LBP hazards Notice to Occupants |
| All other | Pre-1978 | Provision of pamphlet Visual assessment to identify deteriorated surfaces Notice to Occupants Ongoing LBP maintenance as part of operations |

Exempt from LBP Regulations

- Housing built after January 1, 1978

- Housing exclusively for the elderly or disabled, unless small children reside at the housing unit

- Zero-bedroom dwellings: SRO units, dormitories, barracks

- Inspector-certified properties that have been found to be free of LBP

- Properties where LBP removal has been completed

- Unoccupied housing that will be vacant until demolition

- Non-residential properties

- Projects where rehabilitation will not disturb painted surfaces

- Emergency repairs to safeguard against imminent danger to human life, health or safety, or to protect from further structural damage

- Emergency shelters where clients will not stay longer than 100 days

Copies of the Lead-Based Paint regulations can be obtained by downloading it from the HUD Office of Lead Hazard Control web site at www.hud.gov/lea or by calling 1-800-424-LEAD.